## Slide 1
补充测试/Supplementary Test
报告人： 班国帅
报告时间： 2026.04

## Slide 2
1.
异常芯片情况/Abnormal Chip Condition
1#
2#
通讯情况/Communication Status(NG)

## Slide 3
2
引脚电阻/Pin Resistance
PBI-
67.1KΩ
VC4
6.25MΩ
VC3
7.13MΩ
VC2
7.29MΩ
VC1
5.42MΩ
SRN
100.6Ω
SRP
100.6Ω
TS1
9.2KΩ
PRES
9.9KΩ
SMBD
134.7KΩ
SMBC
135.1KΩ
FUSE
20.2MΩ
DSG
14.35MΩ
CHG
17.92MΩ
PCHG
6.51MΩ
BAT
106.3KΩ
PACK
10.55MΩ
备注：未上电。B-对各引脚电阻
Note: Not powered on. Resistance between B- and each pin

## Slide 4
3
引脚电压/Pin Voltage
PBI-
0.011V
VC4
11.35V
VC3
8.49V
VC2
5.63V
VC1
2.761V
SRN
0V
SRP
0V
TS1
0V
PRES
0V
SMBD
0V
SMBC
0V
FUSE
0.020V
PACK
0.0023V
CHG
5.7V
PCHG
10.79V
BAT
11.07V
DSG
0.023V
备注：上电(四串电芯，总电压是11.35V),各引脚对B-的电压
Note: Powered on (4-series cells, total voltage 11.35 V). Voltage of each pin relative to B-.

## Slide 5
3
正常芯片状况
正常芯片丝印/Normal Chip Marking
通讯情况/Communication Status(OK)
备注：按照A-B-A交叉实验验证不良跟随芯片走
Note: Defect follows the chip as verified by A-B-A cross-test.

## Slide 6
Power the Future