描述：

The TLC4541 and TLC4545 are a family of high performance, 16-bit, low power, miniature CMOS analog-to-digital converters (ADCs). These devices operate from a single 5-V supply. Devices are available with single, dual, or single pseudo-differential inputs. All of these devices have a chip select (CS), serial clock (SCLK), and serial data output (SDO) that provides a direct 3-wire interface to the serial port of most popular host microprocessors (SPI interface). When interfaced with a DSP, a frame sync signal (FS) is used to indicate the start of a serial data frame on either pin 1 (CS) or pin 7 (FS) for the TLC4541. The TLC4545 ADC connects

to the DSP via pin 1 only (CS). The TLC4541 and TLC4545 are designed to operate with low power consumption. The power saving feature is further enhanced with an auto-power down mode. This product family features a high-speed serial link to modern host processors with an external SCLK up to 15 MHz. Both families use a built-in oscillator as the conversion clock，providing a 2.94 s maximum conversion time.

TLC4541/45 是高性能家族，16位，低功耗，CMOS工艺AD转换器。5V电源供电。芯片可接受单、双、单伪差分信号输入。芯片有一个片选端CS，串行时钟SCLK，串行数据输出端口SDO，可以和具有SPI接口的微处理器进行三线制连接。如果和DSP连接，同步信号FS可以用来指示串行数据的开始（对于4541而言，FS或者CS都可以）。TLC4545通过CS连接到DSP上。4541和4541都是低功耗设计，通过自动断电模式节省功耗。在外部时钟信号高达15MHz的作用下实现和主机的高速串行连接。内部振荡器作为转换的时钟，实现最大2.94uS的转换时间。

CS： 片选，由高到低的转变可以使SDO从高阻状态变到输出MSB的状态，如果4541连接到DSP，那么CS需要接地。

FS： DSP同步输入。用以只是串行数据的开始，由高到低的变化可以使SDO由高阻状态变到输出MSB状态，如果此引脚未用到，需要连接到VDD。

SDO：3态串行数据输出ad转换的结果。CS为高电平的时候SDO保持高阻态。输出数据的格式是MSB在前。剩下的15位数据在SCLK的上升沿更新。如果FS未激活（当CS下降沿的时候FS=1）：在CS置低一段时间以后，从SDO引脚输出MSB。剩下的数据在SCLK的下降沿有效。如果FS激活（CS下降沿时FS=0）在FS的上升沿从SDO引脚输出MSB，剩下的数据在SCLK的下降沿输出，在上升沿改变（这是和DSP的典型连接方式）。

CS： 片选，由高到低的转变可以使SDO从高阻状态变到输出MSB的状态，当使用DSP的串口时CS输入端可以连接到DSP的FS端口。

SDO：3态串行数据输出ad转换的结果。CS为高电平的时候SDO保持高阻态，在变成低电平之后输出数据，直到输出完LSB。输出数据的格式是MSB在前。剩下的15位数据在SCLK的上升沿更新。输出数据在SCLk的下降沿有效直到所有数据输出。SDO在17个SCLK的上升沿之后恢复到高阻状态。如果第17个SCLK周期没有发生，在和SPI主机连接的情况下，SDO在CS的上升沿恢复到高阻状态。

系统初始化：

The TLC4541/45 each require one RESET cycle after power-on for initialization in order to operate properly.This RESET cycle is initiated by asserting the CS pin (pin 1) low for a minimum duration of at least one SCLK falling edge but no more than 8 SCLK falling edges in length.The RESET cycle is terminated by asserting CS high. If a valid RESET cycle is issued, the data presented on the SDO output during the following cycle is FF00h.This output code is useful in determining when a valid reset/initialization has occurred.The TLC4541 has separate CS and FS pins. In this case, it is also possible to initiate the RESET cycle by asserting FS low if CS is already low. The RESET cycle can be terminated by either asserting CS high (as shown in the first RESET cycle in Figure 14), or by asserting FS high ( as shown in the second RESET cycle in Figure 14), whichever happens first.

TLC4541在上电以后需要一个初始化/重置的过程来保证正常运行。初始化进程是通过拉低CS一段时间（最少一个CLK脉冲，但是不能超过八个），通过拉高CS来终止初始化。如果初始化成功，数据输出端会在接下来的脉冲信号的作用下输出FF00数据，这个数据可以用来判断是否成功完成初始化。TLC4541把CS和FS区分开来，在这种情况下，需要在CS置低的情况下拉低FS来进行初始化。任意拉高FS或者CS都可以终止初始化进程。

采样：

The converter sample time is 20 SCLKs in duration, beginning on the 5th SCLK received during an active signal on the CS input (or FS input for the TLC4541.)

转换器的采样时间是20个CLK周期，在CS置低以后，第5个CLK周期开始采样。

转换：

Each device completes a conversion in the following manner. The conversion is started after the 24th falling SCLK edge. The CS input can be released at this point or at any time during the remainder of the conversion cycle. The conversion takes a maximum of 2.94 s to complete. Enough time (for conversion) should be allowed before the next falling edge on the CS input (or rising edge on the FS input for the TLC4541) so that no conversion is terminated prematurely. If the conversion cycle is terminated early, the data presented on SDO during the following cycle is FF00h. This predefined output code is helpful in determining if the cycle time is not long enough to complete the conversion. The same code is also used to determine if a reset cycle is valid.

每个芯片都按照以下流程完成转换过程：转换过程从第24个CLK的下降沿开始。在这个时候，可以释放CS（或者在剩下的转换周期内任何一个时候拉高CS）。在CS输入下一个低电平之前（或者TLC4541的FS引脚输入上升沿信号）要保证足够的时间以便完成采样而不至于被提前结束转换。如果转换过程被提前结束了，那么在接下来的CLK周期的作用下SDO引脚输出FF00信号，这个输出信号可以用来判断是否给予了足够的时间来完成转换，这种信号也用来判断是否成功完成初始化过程。

采样和转换周期：

TLC4541:

Control via pin 1, CS (FS = 1 at the falling edge of CS)− The falling edge of CS is the start of the cycle. Transitions on CS can occur when SCLK is high or low. The MSB may be read on the first falling SCLK edge after CS is low. Output data changes on the rising edge of SCLK. This control method is typically used for a microcontroller with an SPI interface, although it can also be used for a DSP.

通过控制CS来进行（在CS下降沿时FS处于高电平状态），CS的下降沿就是这个过程的开始，不论SCLK是高还是低，只要CS置低就开始转换。当CS置低以后，MSB出现在第一个SCLK的下降沿。输出数据在SCLK的上升沿变化。这种控制方法典型的应用于与微处理器的SPI接口，当然可以用于DSP。

TLC4545:

All control is provided using the CS input (pin 1) on the TLC4545. Transitions on CS can occur when SCLK is high or low. The cycle is started on the falling edge transition on the CS input. This signal can be provided by either a CS signal (when interfacing with an SPI microcontroller) or FS signal (when interfacing with a TMS320 DSP). The MSB is presented to SDO on the falling edge of the signal applied to pin 1 and may be read on the first falling SCLK edge after this input is low. Output data changes on the rising edge of SCLK.

对于TLC4545，所有的控制都是通过CS实现。不论SCLK是高还是低，只要CS置低，在CS的下降沿就开始转换。这种转换信号可以是由具备SPI接口的单片机通过CS给予，也可以是由DSP通过FS信号给予。当CS置低以后，MSB出现在第一个SCLK的下降沿。输出数据在SCLK的上升沿变化。

控制方式：

control via pin 1 (CS, SPI interface)

All devices are compatible with this mode of operation. A falling edge on the CS input initiates the cycle. (For the TLC4541, the FS input is tied to VDD ). The CS input remains low for the entire sampling time plus 4 SCLK decoding time(16 falling SCLK edges) and can then be released at any point during the remainder of the conversion. Enough time should be allowed before the next falling CS edge so that the conversion cycle is not terminated prematurely.

SPI接口（控制CS）

所有的芯片都兼容于这种工作方式。CS的下降沿初始化这个周期（对于TLC4541而言，FS要接到VDD上）。CS要一直保持低电平直到达到完成采样和4个SCLK的解码（16个SCLK的下降沿）所花的时间，然后才可以被释放成高电平。在下一个CS置低之前，应该保证延时足够的时间来完成转换而不至于被过早的结束。

control via pin 1 (CS, DSP interface)

All devices are compatible with this mode of operation. The FS signal from a DSP is connected directly to the CS input of the ADC. A falling edge on the CS input while SCLK is high or low initiates the cycle. (For TLC4541 in this configuration, the FS input is tied to VDD.) Enough time should be allowed before the next rising CS edge so that the conversion cycle is not terminated prematurely.

DSP接口（控制CS）

所有的芯片都兼容于这种模式。从DSP出来的FS信号直接连到ADC的CS输出脚。在CS的下降沿时开始转换，不论SCLK的状态。（对于TLC4541而言，FS引脚要接到VDD）在下一个CS置低之前，应该保证延时足够的时间来完成转换而不至于被过早的结束。

我自己的理解

整个转换需要的正常步骤：

第一步：

系统通电以后，先进行初始化，初始化需要拉低CS然后给1-8个CLK，然后拉高CS，再拉低CS，如果在SCLK的作用下从SDO输出FF00，则表明初始化成功。（按照手册的描述我认为这一步仅仅是在通电以后进行一次，以后就不需要再运行了，除非断电）

第二步：

采样。拉低CS，在24个CLK后完成采样（看时序图，此时也会从SDO输出数据，但此数据不可取，不是真正的AD转换结果）。

第三步：

转换。拉高CS，并延时。

第四步：

输出转换结果。拉低CS，在SCLK的下降沿输出MSB-LSB，如果第三步延时不够，则输出FF00，如果前三步成功，则输出正确的AD转换结果。