How to build:

- The build is based on mcsdk_2_00_05_17, MCSDK_INSTALL_PATH\tools\boot_loader\ibl\doc\build_instructions.txt is a good start.

- Go to below link to install MinGw from below link and click the latest exe version.

http://sourceforge.net/projects/mingw/files/Automated%20MinGW%20Installer/mingw-get-inst/mingw-get-inst-20110316/mingw-get-inst-20110316.exe/download

If you are installing the MinGW offline, you can try as below diagram shows.

By default it will be installed in C:\MinGW

While installing MinGW following options have to be chosen:

1.  MinGw Compiler Suite

-   C Compiler

2. MinGW Developer Toolkit

- Then we need run “MinGW Shell” to enter Msys shell.

- Once enter Msys shell, the root is C:\MinGW\msys\1.0. Use command “cd /” then “ls” to know where you are.

- Copy folder “ibl” and file “IBL_buildibl” under MCSDK_INSTALL_PATH\tools\boot_loader to C:\MinGW\msys\1.0.

- Before run build script, we need to check “C:\MinGW\msys\1.0\IBL_buildibl” and “C:\MinGW\msys\1.0\ibl\src\make\setupenvMsys.sh”

For IBL_buildibl, you can change “ENDIAN=little” to “ENDIAN=big”

For setupenvMsys.sh, original path below.

# Specify the base directory of the c6000 compiler with UNIX style path separator

export C6X_BASE_DIR='"C:/Program Files/Texas Instruments/C6000 Code Generation Tools 7.2.4"'

# Specify the base directory of the c6000 compiler in format understandable by the MSYS Bash shell

export C6X_BASE_DIR_MSYS=/c/Program\ Files/Texas\ Instruments/C6000\ Code\ Generation\ Tools\ 7\.2\.4

Which can be changed as below based on your C6000 CGT tool install path.

# Specify the base directory of the c6000 compiler with UNIX style path separator

export C6X_BASE_DIR='"C:/Program Files/Texas Instruments/ccsv5/tools/compiler/c6000"'

# Specify the base directory of the c6000 compiler in format understandable by the MSYS Bash shell

export C6X_BASE_DIR_MSYS=/c/Program\ Files/Texas\ Instruments/ccsv5/tools/compiler/c6000

- Then run “IBL_buildibl”

- Build result is under “C:\MinGW\msys\1.0\ibl\src\make\bin”.

How to Burn:

When burning the IBL, pls set EVM as “NO Boot Mode”. It is recommended to use the latest MCSDK, and here assume the written file is i2crom_0x51_c6678_le(be).bin, and the parameter configure file is i2cparam_0x51_c6678_le(be)_0x500.out.

For little endian IBL:

- Set the EVM as little endian and no boot mode;

- Copy your i2crom_0x51_c6678_le.bin to the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin;

- Modify the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin\ eepromwriter_input.txt as below.

file_name  = i2crom_0x51_c6678_le.bin

bus_addr   = 0x51

start_addr = 0

swap_data  = 0

- Connected the CCS with EVM;

- Load the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin\eepromwriter_evm6678l.out

- Load memory 0x80000000 with your own i2crom_0x51_c6678_le.bin;

- Run the project, and when the “EEPROM programming completed successfully” is printed in the console it means the i2crom_0x51_c6678_le.bin has been burned into EEPROM successfully;

- Execute CPU reset and system reset, and load the i2cparam_0x51_c6678_le_0x500.out into the EVM;

- Load the MCSDK_INSTALL_PATH\tools\boot_loader\ibl\src\make\bin\ i2cConfig.gel;

- Run the project, and then execute “setConfig_c6678_main” in the script tools;

- Press enter in the console, and then “I2c table write complete” is printed in the console.

For big endian IBL:

- Set the EVM to little endian and no boot mode;Copy your i2crom_0x51_c6678_be.bin to the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin;

- Modify the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin\ eepromwriter_input.txt as below.

file_name  = i2crom_0x51_c6678_be.bin

bus_addr   = 0x51

start_addr = 0

swap_data  = 0

- Connected the CCS with EVM;

- Load the MCSDK_INSTALL_PATH\tools\writer\eeprom\evmc6678l\bin\eepromwriter_evm6678l.out (still using the little endian *.out file for EEPROM writer)

- Load memory 0x80000000 with your own i2crom_0x51_c6678_be.bin;

- Run the project, and when the “EEPROM programming completed successfully” is printed in the console it means the i2crom_0x51_c6678_be.bin has been burned into EEPROM successfully;

- Power off and Set the EVM as big endian and no boot mode, then power on EVM;

- Connect the CCS with EVM, and load the i2cparam_0x51_c6678_be_0x500.out into the EVM;

- Load the MCSDK_INSTALL_PATH\tools\boot_loader\ibl\src\make\bin\ i2cConfig.gel;

- Run the project, and then execute “setConfig_c6678_main” in the script tools;

- Press enter in the console, and then “I2c table write complete” is printed in the console.