## Slide 1: TMS320x2833x Analog-to-Digital Converter(ADC) Module

## Slide 2
The pin of ADC

## Slide 3: §Features and functions of ADC module：
12-bit ADC core with built-in dual sample-and-hold
Simultaneous sampling or sequential sampling modes
Analog input: 0 V to 3 V

## Slide 4
Fast conversion time runs at 12.5 MHz, ADC clock
16-channel, multiplexed inputs
Sequencer can be operated as two independent 8-state sequencers or as one large 16-state sequencer (i.e.,two cascaded 8-state sequencers).
Sixteen result registers to store conversion values

## Slide 5
Multiple triggers as sources for the start-of-conversion sequence
– S/W - software immediate start
– ePWM 1-6
– GPIO XINT2
Flexible interrupt control allows interrupt request on every end-of-sequence (EOS) or every other EOS
Sequencer can operate in "start/stop" mode Sample-and-hold (S/H) acquisition time window has separate prescale control

## Slide 6: §Block diagram of ADC Module

## Slide 7: §The relevant register of ADC

## Slide 9: §Autoconversion Sequencer Principle of Operation(According to the Conversion mode)
1. Cascaded Mode

## Slide 10
Simultaneous Sampling Cascaded Sequencer Mode Example

## Slide 11
2. Dual Sequencers

## Slide 12
Simultaneous Sampling Dual Sequencer Mode Example

## Slide 13: §Comparison of Single and Cascaded Operating Modes

## Slide 14: §ADC Clock Prescaler
ADC Core Clock and Sample-and-Hold (S/H) Clock

## Slide 15: §ADC-module Clock and Sample Rate
Clock Chain to the ADC

## Slide 16: § Low-power Modes

## Slide 17: register
struct ADCTRL1_BITS { // bits description Uint16 rsvd1:4; // 3:0 reserved Uint16 SEQ_CASC:1; // 4 Cascaded sequencer mode Uint16 SEQ_OVRD:1; // 5 Sequencer override Uint16 CONT_RUN:1; // 6 Continuous run Uint16 CPS:1; // 7 ADC core clock pre-scalar ADC Uint16 ACQ_PS:4; // 11:8 Acquisition window size Uint16 SUSMOD:2; // 13:12 Emulation suspend mode Uint16 RESET:1; // 14 ADC reset ADC Uint16 rsvd2:1; // 15 reserved };

## Slide 18
struct ADCTRL2_BITS { // bits description Uint16 EPWM_SOCB_SEQ2:1; // 0 EPWM compare B SOC mask for SEQ2 Uint16 rsvd1:1; // 1 reserved Uint16 INT_MOD_SEQ2:1; // 2 SEQ2 Interrupt mode Uint16 INT_ENA_SEQ2:1; // 3 SEQ2 Interrupt enable Uint16 rsvd2:1; // 4 reserved Uint16 SOC_SEQ2:1; // 5 Start of conversion for Uint16 RST_SEQ2:1; // 6 Reset SEQ2 SEQ2复位 Uint16 EXT_SOC_SEQ1:1; // 7 External start of conversion for SEQ1 Uint16 EPWM_SOCA_SEQ1:1; // 8 EPWM compare B SOC mask for SEQ1

## Slide 19
Uint16 rsvd3:1; // 9 reserved Uint16 INT_MOD_SEQ1:1; // 10 SEQ1 Interrupt mode Uint16 INT_ENA_SEQ1:1; // 11 SEQ1 Interrupt enable Uint16 rsvd4:1; // 12 reserved Uint16 SOC_SEQ1:1; // 13 Start of conversion trigger for SEQ1 Uint16 RST_SEQ1:1; // 14 Restart sequencer 1 Uint16 EPWM_SOCB_SEQ:1; // 15 EPWM compare B SOC enable };

## Slide 20
struct ADCASEQSR_BITS { // bits description Uint16 SEQ1_STATE:4; // 3:0 SEQ1 state Uint16 SEQ2_STATE:3; // 6:4 SEQ2 state Uint16 rsvd1:1; // 7 reserved Uint16 SEQ_CNTR:4; // 11:8 Sequencing counter status Uint16 rsvd2:4; // 15:12 reserved };

## Slide 21: The ADC conversion software steps:
1. Initialize the DSP system; 2. Set the PIE the interrupt vector table, 3. Initialize the ADC module; 4. The ADC interrupt entry address into PIE interrupt vector table, open the interrupt; 5. Software to start the ADC conversion; 6. The ADC interrupt; 7. Read the ADC conversion results in the ADC interrupt, software to start the next ADC interrupt.

## Slide 22
struct ADCMAXCONV_BITS { // bits description Uint16 MAX_CONV1:4; // 3:0 Max number of conversions Uint16 MAX_CONV2:3; // 6:4 Max number of conversions Uint16 rsvd1:9; // 15:7 reserved };

## Slide 23
struct ADCTRL3_BITS { // bits description Uint16 SMODE_SEL:1; // 0 Sampling mode select Uint16 ADCCLKPS:4; // 4:1 ADC core clock divider Uint16 ADCPWDN:1; // 5 ADC powerdown Uint16 ADCBGRFDN:2; // 7:6 ADC bandgap/ref power down Uint16 rsvd1:8; // 15:8 reserved };

## Slide 24
struct ADCST_BITS { // bits description Uint16 INT_SEQ1:1; // 0 SEQ1 Interrupt flag Uint16 INT_SEQ2:1; // 1 SEQ2 Interrupt flag Uint16 SEQ1_BSY:1; // 2 SEQ1 busy status Uint16 SEQ2_BSY:1; // 3 SEQ2 busy status Uint16 INT_SEQ1_CLR:1; // 4 SEQ1 Interrupt clear Uint16 INT_SEQ2_CLR:1; // 5 SEQ2 Interrupt clear Uint16 EOS_BUF1:1; // 6 End of sequence buffer1 Uint16 EOS_BUF2:1; // 7 End of sequence buffer2 Uint16 rsvd1:8; // 15:8 reserved };

## Slide 25
struct ADCREFSEL_BITS { // bits description Uint16 rsvd1:14; // 13:0 reserved Uint16 REF_SEL:2; // 15:14 Reference select };
struct ADCOFFTRIM_BITS{ // bits description int16 OFFSET_TRIM:9; // 8:0 Offset Trim Uint16 rsvd1:7; // 15:9 reserved };