## Slide 1: Key Capacitor Specifications
Tolerance
Voltage rating
Temperature range
Temperature Drift
Voltage Coefficient
ESR
ESL

## Slide 2: Capacitors
Type
  Ceramic
  Tantalum Electrolytic Capacitors (Polarized)
  Aluminum Electrolytic Capacitors (Polarized)
  Polystyrene Film Capacitors
  Polyester Film Capacitors
  Polypropylene Capacitors
  Mica Capacitors

## Slide 3: Ceramic Capacitors
COG (NP0)
  Low temperature coefficient
  Low voltage coefficient
  Low change in capacitance over frequency
  High tolerance
  Temperature range (-55C to 125C)
  Use in signal path, filtering, precision applications
X7R
  Worse then COG for temperature drift, voltage coefficient
  Worse then COG for change over frequency
  Lower tolerance then COG
  Temperature range (-55C to 125C)
  Use for decoupling, and other non critical applications
  piezoelectric effect
Y5V
  Worse characteristics then X7R
  Limited temperature range (-30C to 85C)