## Slide 1: HerculesTM 安全微控制器平台
新产品简介(上)
Notes: Hello and welcome to an overview of the new Hercules Safety Microcontroller platform.

## Slide 2
2011年9月6日，TI发布了2款最新的Hercules系列微控制器 RM48x & TMS570LS31x
  使用ARM Cortex内核的Hercules系列微控制器 是专门为一些安全关键类型的应用比如医疗，工业和运输等开发设计的。
  RM48x 和 TMS570 微控制器内置了很多安全特性，包括以锁步模式运行的双Cortex-R4F内核，内置的CPU和RAM自检，针对Flash和系统RAM的ECC模块，以及先进的错误信号模块以回报错误信息。
    产品系列包括34 款最新的MCU，工作频率从80 MHz 到 220 MHz
    后续将发布所有产品的开发套件和样品
  RM48x系列微控制器内置了互联型外设 ：CAN, Ethernet和USB (主机 & 设备)
  TMS570系列微控制器支持汽车通信协议：Us support the automotive communication protocols: LIN, CAN和FlexRay.
概述
Notes: So to get started, a quick summary. On September 6th of 2011, Texas Instruments announced the Hercules platform of microcontrollers and that consists of two new large microcontroller families, the RM48x and the TMS570LS31x generation of microcontrollers. It's also going to have a third family, the TMS470M family. And at a high level, these are ARM Cortex-based microcontrollers specifically designed for safety critical, medical, industrial, and transportation applications. RM48 and 570s include several built-in safety features, including dual Cortex-R4F CPUs running in lockstep, built-in self-tests for the CPU and RAM, ECC for all of the RAM and the flash, and the error signaling module, as well, and I'll go in to some more details on those safety features later in the presentation.
On September 6th, we will have a total of 34 new microcontrollers and the speeds are going to be ranging from 80 MHz all the way up to 220 MHz. We are also going to have development kits and samples of the new superset devices available as soon as we launch coming up next week in September. The RM48, specifically, microcontrollers will have connectivity peripherals like CAN, Ethernet, and USB. The TMS570 microcontrollers are going to be more automotive and transportation centered and they're going to have communication protocols like LIN, CAN, and FlexRay and so those materials has NDA content for the next week or so since we're not launching and publicly announcing this information until September 6th.

## Slide 3: HerculesTM 系列微控制器引领世界走向安全
EN 50128
(railway)
DO-254 DO-178B (aerospace)
IEC 50156 (furnaces)
IEC 60880 (nuclear power stations)
IEC 60601 (medical equipment)
ISO 26262 (automotive)
IEC 62061
ISO 13849 (machinery)
IEC 61511 (process industry)
IEC 61508
(safety)
预防随机的和系统性的错误
为不同安全应用之间的差异性留出余量
简化安全应用的开发和认证过程
Hercules 微控制器提供用户：
安全至上的
应用体验
在一些安全至上的应用中，电子产品的使用正在激增
3
Hercules
MCU
TM
Notes: So to give you an overview as to why it makes sense to release the Hercules to a really broad market, it has to do with the market in general. There have been several safety standards that have popped up in the past few years and they’ve been getting a lot of attention recently and these are international standards, so IEC standards and ISO standards. And they're very centered around safety and lots of end customers or even government bodies have actually been mandating that a lot of products actually comply with these international standards. And so this slide here kind of gives an overview of just some of the standards that exist around the world and the industries that they apply to. So, in general, down at the bottom of this image on the world, the IEC 61508 standard is a general safety standard that can apply across many industries and it is meant to apply to industries that don’t have a specific standard.
And so Texas Instruments has actually been concentrating on this standard with our TMS570 microcontrollers for a number of years. And just to give you a little background on our group, we actually come from the automotive microcontroller group and we've had over 20 years of experience doing microcontrollers for safety-critical automotive applications like airbag, anti-lock brakes, stability control, and our automotive customers are the ones that first concentrated on this standard and we basically built our architecture to comply with this standard. And then over the years, other standards have emerged, specifically in automotive the ISO 26262 standard and then as you can see there's a number of other standards that apply to specific industries where the TMS570 and RM48 fit very well into those safety-critical applications and what makes Hercules different than a standard microcontroller as far as safety goes. So the architecture gives protection against random and systematic faults. It also provides headroom for application differentiation because we have so many safety features built in the hardware, our customers do not have to use a lot of the CPU power or their program space for doing the safety part of the application, so there's room to actually develop more of their applications specifically. And then also we provide simplified development systems certification so that they don’t have to develop a lot of safety algorithms themselves and then also we provide full safety documentation to them so that it makes their certification process easier.

## Slide 4
4
TI HerculesTM 微控制器平台 ARM® Cortex 内核微控制器
超值系列
运输和安全
微控制器
Hercules 平台
TMS470M
TMS570
RM4x
高性能
工业和医疗安全
微控制器
工业应用
医疗应用
-40 到 105°C 工作范围
以太网，USB互联外设
专为安全标准设计
    IEC 61508 SIL-3
Cortex-R内核 – 超越 350 DMIPs
高性能
安全运输
微控制器
运输应用
汽车 Q100 认证
-40 到 125°C 工作范围
LIN, CAN 互联外设
专为安全标准设计
  IEC 61508 Systems
Cortex-M – 高达 100 DMIPS
运输应用
汽车 Q100 认证
-40 到 125°C 工作范围
FlexRay, CAN 互联外设
专为安全标准设计
  ISO 26262 ASIL-D
  IEC 61508 SIL-3
Cortex-R 内核– 超越 280 DMIPs
34 款
MCUs
Notes: 4
4
4
4
The whole platform consists of three subfamilies, the first one being the RM4, which is actually brand new. We've never had any RM4 products before. So this is brand new. The TMS570, if you're familiar with it, you’ve probably known that it has gone in automotive specifically in the past and it's not just for automotive anymore. TMS570 is now targeted at high performance transportation applications. The third leg of the Hercules platform is the TMS470M line, and these microcontrollers are the value line targeted at transportation safety applications and general safety applications, as well.
The RM48 provides high performance microcontrollers specifically for industrial and medical applications. Temperature range on these devices are -40 to 105 C and from a communications point of view, the things to highlight are they do have 10/100 Ethernet and USB host and device connectivity. And these are developed for safety standard level IEC 61508 SIL-3 level and it is – from a core perspective, it uses the ARM Cortex-R4 floating point CPU that provides over 350 DMIPS of performance. And this product line has the highest performance ARM core microcontroller and TIs portfolio.
On the TMS570 side, like I said for high performance transportation applications, these are all automotive Q100 qualified. They are -40 to 125 C ambient temperature operation. From a network point of view, they feature the FlexRay and CAN connectivity, along with some of the other automotive connectivity options like LIN. And from a safety features point of view, these are developed to ISO 26262 ASIL-D level and also the IEC 61508 SIL-3 and these also feature the ARM Cortex-R4 floating point CPU providing over 280 DMIPS of performance.
On the TMS470 line, again, this is our value line so a lower cost point for applications not needing the performance or flash memory size of the TMS570 or the RM and not needing the full level of safety that’s provided by either the RM or 570. So these are transportation or general safety applications. These are also automotive Q100 qualified temperature spec -40 to 125 C and these have LIN and CAN connectivity. And these can support safety systems for different levels of IEC 61508 and these are based on the Cortex-M3 CPU providing up to 100 DMIPS of performance.

## Slide 5: HerculesTM RM48 专注安全MCU 最高性能的ARM ®微控制器
高性能的实时控制
预防随机性和系统性的错误
安全认证和高可靠性
其他…
  系统可扩展
  系统安全和成本的综合考量
  软件代码的可移植性
面向应用的需求
ARM® Cortex™-R4F 浮点CPU
高达220MHz (>350 DMIPS)
专为安全至上的工业和医疗应用设计
高达3MB的内置FLASH
CAN, Ethernet, USB 主机/设备 等外设
- 40°C 到 105°C 工作范围
新特性！
RM48 – 专注于工业和医疗安全
5
Notes: 5
Moving on, let’s highlight the RM48 specifically. This is where we're focusing a lot of our energy and attention on since this is a totally new product family never been announced before. So this is the first time that the public is going to hear about it on September 6th, and these are some of the features that it has. So, like I've mentioned, this is the highest performance ARM-based microcontroller that TI has based on the ARM Cortex-R4 floating point CPU. They'll have clock speeds of up 220 megahertz providing over 350 DMIPS of performance, and specifically for safety-critical, industrial and medical systems. Embedded flash memory going up to 3 megabytes on this family and then as I mentioned CAN, Ethernet, USB host and device and temperature range is the industrial -40 C to 105 C. And these are very well suited for high performance real time control applications that also need protection against random and systematic faults inside the microcontroller. So safety certification and high reliability is a feature here and it's a very good fit for safety-critical industrial and medical applications.

## Slide 6
稳定的控制
助力转向
汽车 充电
ABS
助力转向
被动性安全
超值
运输
锁步 CPUs
ISO
26262 support planned
Sampling
Development
TMS570LS102S
1MB, 160kB
TMS570LS202S
2*R4F LS
2MB, 160kB
160MHz
TMS470MF031S
320kB, 16kB
TMS470MF066S
ARM® Cortex™-M3
640kB, 48kB
80MHz
TMS470MF042S
448kB, 24kB
TMS570LS31x
2*R4F LS
3MB, 256kB
180MHz
TMS570LS21x
2MB, 192kB
较小的存储器
新的外设
低成本
6
IEC
ISO
IEC
61508 SIL3
Production
工业和医疗
RM48x
2*R4F LS
3MB, 256kB
220MHz
RM48x
2MB, 192kB
ETHERNET
IEC
安全型
马达控制
工业控制 自动化控制
安全型 互联通信
医疗
Hercules™ 安全性MCU路线图
大的存储器
新的外设
更大的存储器
新的外设
ETHERNET
IEC
Production 1Q 2012
Production 1Q 2013
Notes: This is our road map basically showing where we are today as far as products in the Hercules family and these are divided into three main sections here. Down at the bottom, the value line in the middle, the high performance transportation, and then up at the top, the industrial and medical. So start down at the bottom with the value line. This is the TMS470Ms, so these are the Cortex-M3 based microcontrollers. These devices have flash ranges between 320K up to 640K and the superset device is in production today highlighted by the green on here and then we've got two other devices in this family that will be in production in the first quarter of 2012 and these are the smaller memory footprint devices. These are all in compatible 100 pin QFPs.
Then moving up to the transportation section, these are the TMS570 microcontrollers that were announced a little over a year and a half ago. These are based on the Cortex-R4F CPU running in lock-step. There are 1 megabyte and 2 megabyte flash footprints available with 160K of RAM and these are running up to 160 MHz So these are microcontrollers that were designed for automotive specifically, but they have fit very well into other transportation applications like railway, aerospace, off road vehicles, and we've seen quite a lot of success and interest for these microcontrollers since we've launched them a year and a half ago.
And in that last year and a half or really more like two years, we've taken these devices out and we've talked to customers from the other industries, for example, medical and industrial, and they really liked the safety concept of TMS570 and they’ve also liked the certification documentation that we provide with TMS570. But they’ve told us you're missing a few things to be the perfect microcontroller for us. And so we've listened to those customers and specifically for industrial and medical and we've come up with the RM48 line and that’s up here on the top. It's industrial and medical and these are some of the devices that are going to be announced on September 6. So these are also featuring same safety concept as TMS570 using the lock-step Cortex-R4 floating point CPU. One of the things that customers ask for was more program space, so more flash memory. So these devices are going up to 3 megabytes. With that, they’ve also asked for more RAM, so we're going up to 256K on the RAM.
Other things that they’ve asked for is USB. That’s been a huge one. So we've added USB host and device to these microcontrollers. And then a big one, probably the largest one that they’ve been asking for is the Ethernet. So we've added 10/100 Ethernet to these devices, as well. And these also, like I had mentioned, same safety concepts and architecture as TMS570 for IEC 61508 SIL-3 level applications. Then also we're coming out with some new devices as well on September 6 in the TMS570 family. These devices are also based on the same core, going to have 3 megabytes of – up to 3 megabytes of flash, 256K of RAM, and 180 MHz max speed on the Cortex-R4 CPU. And from a peripheral standpoint, they're going to have the same peripherals as the previous generation TMS570, but we're also adding a 10/100 Ethernet option, as well.
And these are designed using the ISO 26262 flow for as far as safety goes and then they're also very well suited for IEC 61508 applications. And then we have several new devices planned going out in the future in all families. So for the industrial and medical, we're going to have more memory options, new peripherals coming out, same thing for the TMS570 high performance transportation, and then in the value line we're transitioning over all of our new devices to use the Cortex-R4 CPU. So these devices over here on the left side in the value line are going to be the last ones that used the Cortex-M3.
6

## Slide 7: Hercules Cortex-R4F MCU 的安全特性
面向锁步双核的
失效防护监测
面向 flash 和 RAM的ECC模块
以及Cortex-R4F内部互联
所有的外设，DMA和中断控制RAM都带有奇偶校验
所有RAM都配备 BIST
以便在启动时进行存储器的快速测试
CPU 自检测模块
无需软件介入
IO环回检测
ADC自测…
错误信号模块
外接输出引脚
内置时钟和电源
监测监控模块
专为降低共性错误而
设计优化的
逻辑和物理上的排布
硬件诊断的安全岛 (红色)
软硬件交互监测 (蓝色)
无需安全特性的功能模块 (黑色)
PBIST/LBIST
OSC PLL
POR
CRC
RTI/DWWD
ESM
Enhanced System Bus and Vectored Interrupt Module
DMA
Memory
Flash
w/ ECC
Embedded Trace
RAM
w/ ECC
Power, Clock, & Safety
Memory Interface
External Memory
JTAG Debug
Calibration
ARM® Cortex™-R4F
ARM® Cortex™-R4F
Serial Interfaces
Network Interfaces
Dual ADC
Cores
Dual High-end Timers
GIO
Flash
EEPROM w/ ECC
Fail Safe Detection
串行和通信外设都内置奇偶校验或CRC校验
双 ADC内核
共享通道
7
Notes: Moving on to the safety features. So this is a huge differentiating factor in the Hercules microcontrollers. These have been built ground up in the architecture for safety-critical applications. And at the core of this is the safe island, if you will, so everything on this slide that’s highlighted in red is part of the safe island. So this is hardware that’s heavily safe. There's a lot of redundancy and safety logic built into these modules inside the device. And the idea is if you safe your core or your safe island, you have an execution engine that is known good and then you can use that execution engine to safe other features, and that goes into the blue areas where you have blended hardware, software diagnostics. And then the black areas in here are non-safety critical modules like JTAG, calibration, debug, those sorts of things.
We're going to concentrate on the red areas right now to give you an idea of how the Hercules architecture is different from a standard microcontroller from a safety point of view. So at the heart of that is the lock-step dual core CPUs. So when I say dual core, a lot of people listen to that and think, “Oh I've got two cores that connects different code.” That’s not the case in a lock-step architecture. The second CPU in lock-step architecture is there primarily for redundancy. So from a programmer’s model, there is a single CPU. They never see the second CPU. It's there specifically for monitoring and providing redundancy to the first CPU. That’s this right here, dual core lock-step, and it does have fail safe detection. So that’s the core compare module that constantly compares the outputs of both of the CPUs, and if anyone ever does anything differently, it reports back to the hardware error signaling module that has a dedicated pin to the outside world to let the system know that something has critically gone wrong in the core execution into the microcontroller and appropriate action needs to be taken.
Another key point of the architecture is the flash and the RAM all have ECC or Error Correction Code protection on them. So the ECC is capable of detecting and correcting single bit errors and it's also capable of detecting double bit errors. And one point of reference, we actually do test our microcontrollers at the Los Alamos labs in New Mexico, so we bombard them with the particle accelerator, and in testing, we have seen the ECC being very effective at detecting and correcting single bit errors and we have actually never experienced a double bit error in our testing. And part of the reason for that is this bullet over here on the left-hand side, the logical and physical design optimized to reduce the probably of common cause failure. So the way the RAMs and the flash are laid out, there are no physical bits adjacent to each other in a single logical word, and so that provides optimal ECC protection.
The other thing to note in this logical physical design is the cores themselves so the ARM Cortex-R4F, they're actually physically separate cores that are spaced differently or spaced apart on the die of silicon and the second core is actually flipped and rotated physically in the design on the piece of silicon. So we don’t allow the gates of the CPUs to intermingle on the silicon and that also helps reduce the probability of a common cause error. We also have built-in self-test engines inside the device to test the CPU and we also have a built-in self-test to test all of the RAMs inside the device, and these are hardware BISTs or built-in self-test engines that require a couple of registered configs to kick off so there's not software that has to be – or not a lot of software that has to be generated to test the CPUs and test the RAM inside the device and these are executable either at start up or they actually can be executed periodically in the application.
So we have some customers that have a very long on times where a diagnostic test is needed periodically in the application, for example, some industrial customers where their on time is in the number of years. These types of applications do require having periodic self-test running the application and we can do that, we can support that with this architecture. Other things to highlight is we have on chip clock and voltage monitoring inside these devices, so the PLL of the device actually has a slip detector that if the microcontroller PLL ever slips, it can be detected and the device can either be reset or the clock can be set to a limp mode where it can power the device or run the device’s clocks off of the oscillator or one of the two low power oscillators that are integrated inside the device.
We also have a monitor on the oscillator itself so the external crystal or resonator that’s connected to the device, if the frequency is ever detected above or below a specified range, the microcontroller will automatically detect that and then can either revert to running off of one of the low power oscillators inside the device in a limp mode or it can reset the microcontroller. Also, a key concept is this hardware error signaling module with an external error pin, so all the errors that can be detected inside the device are actually tied to this error signaling module and depending on the severity will either automatically toggle that pin or, for less severe errors, you can choose to just generate and interrupt or you can choose to generate and interrupt and toggle that pin. So for those less critical errors, they are software programmable as far as what action is taken.
Moving on to the blue area of this diagram, these are the blended hardware software diagnostics and these are primarily on the peripheral pins or peripheral modules onside the device, so there is parity on all peripheral DMA and interrupt controller RAMs inside the device. Also, there is either parity or CRC actually built in to the communication peripherals inside the device. We also have loopback testing for the IO modules, the analog to digital converter has a self-test in it, and then also one feature to highlight is that we actually have dual analog to digital cores inside this architecture and there are actually shared channels in between both of the cores so that safety critical voltages on the board can actually be sampled on a single pin but brought out to both of the A to D cores, sampled simultaneously and then compared for redundancy purposes.