## Slide 1: HerculesTM 安全微控制器平台
新产品简介(下)
Notes: Hello and welcome to an overview of the new Hercules Safety Microcontroller platform.

## Slide 2: 高性能的Cortex-R4F 浮点 CPU
高达 220 MHz 的CPU 工作频率
单精度/双精度
IEEE 754 浮点单元
超级架构, SIMD, 8级流水线
高达1.6 DMIPS/MHz
快速乘法，除法，
和平方根运算单元
简化实现算法
8 个分割区域的
存储器保护器
浮点运算和
整数运算并行进行
高达 350 DMIPS 的性能
高性能浮点运算
基于ARM: 被广泛行业采用
ARM ® v7R CortexTM ISA
完全向下兼容 ARM7/9/11
支持 ARM, Thumb 和Thumb-2 指令集
锁步双核CPU：
单核编程模式 –
第二个内核用于检验第一个内核的运算结果
ARM® Cortex™-R4F
220 MHz
2
广泛的 ARM IDE /
编译器支持:
CCS, KIEL, IAR, etc…
TI有多种配置的基于ARM的控制器:
Stellaris, TMS470M, TMS570 & Sitara
Notes: Moving on to some specific details on the Cortex-R4 floating point CPU: So, some of the things to highlight on here is one, it is ARM and there is a lot of support from third parties in the ARM community and with that over here on the lower left-hand corner, that provides us several integrated development environments and compilers available to our customers. So, people aren't tied specifically to Code Composer Studio if they don’t want to be. They also have options from Keil and IAR and then there's several others that people are using. The primary ones that we're highlighting are Keil and IAR and we've worked very closely with them to make sure that we've got good support for our Cortex-R4-based CPUs.
Moving on to some of the more performance-related and safety features of the ARM Cortex-R4, so there's an eight-region memory protection unit inside the device so that’s user programmable to block out different regions of the memory space of the microcontroller so that the core can't accidentally write into those areas. There's also a fast multiply, divide, and square root function built in to the core. On the RM48, like I mentioned previously, clock speeds up to 220 MHz. And then also the instruction set that this core supports is spectacular from a legacy and for a current and going forward standpoint, so it actually does execute the older ARM instructions so ARM7 and ARM9, ARM11, it does execute that instruction set and this is important to a lot of customers that may have legacy code or legacy binary files that have been safety certified or they’ve just been through a long certification process and they don’t want to touch those algorithms and they want to have an ARM core that will execute them.
This core will execute those older algorithms written in that instruction set without a recompile and recertification, so these are in lock step like I had mentioned previously where the second core is checking the first one. And then also from an instruction set point of view, they support the current or the going forward or future instruction set so supporting ARM, Thumb and Thumb-2 instruction sets. So that’s the instruction set, the Cortex-M3 and then also the Cortex-A8 and the A9s execute this Thumb-2 instruction set. Then the R4 also has a built-in single and double precision IEEE 754 compliant floating point unit. The floating point and integer instructions operate in parallel and the R4 actually has a very advanced eight-stage pipeline and it delivers 1.6 DMIPS per megahertz of performance.
And this pipeline is extremely advanced in that it also has branch prediction, so in C code if you're executing a ‘for loop’ and you're taking a specific branch pretty consistently, what the core will do is it will use that branch prediction unit to say that “Hey, the last two or three times that I took this branch, I’m probably going to take that branch the same way again,” and it will actually start prefetching as if that branch is going to be taken, so that increases performance quite tremendously. And then also noticing the highlight is, you know, it is ARM and not only is there or are there a lot of ARM options in the world, but there's also a lot of ARM options specifically from TI. So some of those being the Stellaris based on the Cortex-M3 and then the new C2000 offering, Concerto,that also features the Cortex-M3, and then from the Hercules group, we have the TMS470M value line, we have the TMS570 and then the RM4. And then also moving up into the high end application processors, the Sitara line and some of the OMAP processors also have ARM-based solutions.

## Slide 3: TI 的ARM产品世界
Performance + Integration
ARM9 & Cortex™-A8
Stellaris MCUs
Sitara MPUs
20 MHz – 100 MHz
StellarisWare® 基于ROM
$1.00起售
内置互联通信外设
高性能处理器
强健的多媒体性能
交付移动的计算经验
Cortex™-M3
MPUs
MCUs
Cortex™-R4F
Hercules MCUs
实时控制
浮点
高可靠性
内置丰富冗余
关注安全
> 400 DMIPs
<150 DMIPs
Embedded Flash
HL Operating System
100 – 350 DMIPs
Real time
Embedded
3
Notes: 3
3
So where does the R4 fit in to this TI family? So on the left-hand side you have Stellaris microcontrollers built on the Cortex-M3, those providing less than 150 DMIPS of performance, but they do have embedded flash memory. Hercules fits right into the middle of TIs ARM portfolio with the Cortex-R and Cortex-R4F so providing 100 to 350 DMIPS of performance, very good for real time control applications, applications requiring floating point, very high reliable built-in redundancies and safety focus. And then on the higher end, you have the Sitara MPUs providing over 400 DMIPS of performance and running high level operating systems. So basically the question about the Cortex-R4, where does it fit in to TIs ARM portfolio? It's right in the middle.

## Slide 4
4
性能 / 存储器
高达220 MHz ARM Cortex-R4 浮点内核
高达3MB Flash 和 256KB Data SRAM
16 个通道 DMA
特性
安全
  双锁步内核
  内置自检逻辑的CPU(LBIST)
  支持ECC的Flash & RAM
  内置自检的存储器 (PBIST)
  CRC
  支持奇偶校验的外设RAM
互联通信
  10/100 EMAC
  USB: 主机 / 设备
  3 个CAN
  3 个多路缓冲SPI和2个标准SPI
  2 个 UART
  1 个I2C
高级I/O控制
2个高端定时器协处理器 (NHET)
  高达 40个引脚和6路监控通道
  所有引脚都能生成高精度PWM 或输入捕获/输出比较
  专用的DMA
2 x12位多级缓冲ADC
  24个输入通道
  连续转换模式
  校验和自检
16 个专用GPIO
  所有引脚都能生成外部中断
Fail Safe
Detection
RM48x
POR
OSC PLL
PBIST
LBIST
RTI/DWWD
CRC
Enhanced System Bus and Vectored Interrupt Module
DMA
Packages: LQFP: 144pin -20x20; nfBGA: 337 pin-16x16, 0.8mm; -40 to 105°C Temperature Range
Power, Clock, & Safety
Memory Interface
SDR / ASYNC EMIF
目标应用
工业安全和控制
安全关键的医疗
ARM® Cortex™-R4F
160MHz
ARM® Cortex™-R4F
Up to 220 MHz
Timers / IO
MibSPI1
128 Buffers; 6 CS
Serial I/F
Network I/F
10/100 EMAC
ADC
MibADC1
64 Buffers
12-bit, 24ch
(16ch shared)
GIOB/INTB (8)
3x CAN (64mbx)
MibADC2
64 Buffers
12-bit, 16ch
(16ch shared)
2x UART (LIN1)
2x High End Timer
(NHET)
160 words
NHET1 - 32 ch
NHET2 – 14 ch
MibSPI3
128 Buffers; 6 CS
GIOA/INTA (8)
I2C
SPI2 (2CS)
SPI4 (1CS)
MibSPIP5
128 Buffers; 6 CS
RM48x 框图
双锁步ARM Cortex-R4F 浮点内核
USB 1.1
Host & Device
Enhanced System Bus and Vectored Interrupt Module
DMA
  Note :Above reflects max configuration of each module – some functions are multiplexed.
Memory
3MB Flash
w/ ECC
Calibration & Trace
256 KB RAM
w/ ECC
JTAG Debug
64KB Data Flash
EEPROM w/ ECC
Memory Protection
Notes: Now, I want to go into some of the specifics of the RM48. So this is the block diagram of this family here. I've already mentioned a lot of the performance aspects of this device and the safety features. From a communications point of view, the new exciting things are the new peripherals to this family, the 10/100 Ethernet and the USB host and device. This family also has a three CAN interfaces. It has a total of five SPIs, three of them being multi-buffered so having a RAM around the SPIs and then also two standard SPIs. These devices also have two UARTs and one I2C. From an I/O point of view, there are two High End Timer co-processors inside these devices, so these are very good at timing functions, for example, generating high resolution pulse width modulated signals or doing input capture and compare and these are their own micro engine. So these have their own CPU that execute their own instruction set and are extremely versatile and we have development tools for these modules in particular with built-in examples and algorithm or code palette built in there to help new users get going with the high end timer very quickly. We hear feedback from advanced users of this module. They absolutely love the programmability and the versatility that it provides. The new users are sometimes daunted by it thinking, you know, “Hey, I've got to learn a whole new instruction set and I've got a whole other CPU to program,” and that’s why we have the High End Timer Integrated Development Environment which is a software that runs on the user’s PC that helps people get going with the High End Timer easily and quickly. Like I said it's got built-in algorithm libraries and examples inside of it.
There's also a dedicated DMA for the High End Timer. So there's a secondary DMA that’s for this module so that you're not tying up your CPUs or even the main system DMA to transfer data in and out of the High End Timer. We also have dual 12-bit multi-buffered analog to digital converters so a total of 24 channels. And like I said there's two of them so there's actually a subset of 16 channels that are shared between them. And they also offer continuous conversion mode and then there's also a calibration and self-test mode for the analog to digital converters. Then there's also 16 dedicated general purpose I/O pins in the RM48 and all of these are capable of generating interrupts to the CPU from an outside source. These devices are available in 144-pin QFP and 337 BGA packages. And like I previously mentioned, they are capable of operation in the industrial temperature range of -40 C to 105 C.

## Slide 5
性能 / 存储器
高达180 MHz的 ARM Cortex-R4 浮点内核
高达3MB Flash 和 256KB Data SRAM
带ECC的 64KB Data Flash (模拟EEPROM )
16 Channel DMA
特性
安全
  双锁步CPU内核
  内置自检逻辑的CPU(LBIST)
  支持ECC的Flash & RAM
  内置自检的存储器 (PBIST)
  CRC
  支持奇偶校验的外设RAM
互联通信
  10/100 EMAC
  带专用DMA的FlexRay
  3 个CAN
  3 个多路缓冲SPI + 2 个标准SPI
  2 个UART – 1个支持LIN 2.1
  1个 I2C
高级I/O控制
2个高端定时器协处理器 (NHET)
  高达 40个引脚和6路监控通道
  所有引脚都能生成高精度PWM 或输入捕获/输出比较
  专用的DMA
2 x12位多级缓冲ADC
  24个输入通道
  连续转换模式
  校验和自检
16 个专用GPIO
  所有引脚都能生成外部中断
POR
OSC PLL
PBIST
LBIST
RTI/DWWD
CRC
Enhanced System Bus and Vectored Interrupt Module
DMA
Memory
3MB Flash
w/ ECC
Calibration & Trace
256 KB RAM
w/ ECC
Packages: LQFP: 144pin -20x20; nfBGA: 337 pin-16x16, 0.8mm; -40 to 125°C Temperature Range
Power, Clock, & Safety
Memory Interface
SDR / ASYNC EMIF
JTAG Debug
目标应用
高端 IEC61508和ISO26262安全类应用
车身底盘控制
高端ESC
ARM® Cortex™-R4F
160MHz
ARM® Cortex™-R4F
Up to 180MHz
Timers / IO
MibSPI1
128 Buffers; 6 CS
Serial I/F
Network I/F
10/100 EMAC
ADC
MibADC1
64 Buffers
12-bit, 24ch
(16ch shared)
GIOB/INTB (8)
3x CAN (64mb)
MibADC2
64 Buffers
12-bit, 16ch
(16ch shared)
2x UART (LIN1)
2x High End Timer
(NHET)
160 words
MibSPI3
128 Buffers; 6 CS
GIOA/INTA (8)
I2C
SPI2 (2CS)
SPI4 (1CS)
MibSPIP5
128 Buffers; 6 CS
TMS570LS31x ARM® Cortex™-R4F 浮点内核
2 ch FlexRay
8K Message RAM
64KB Data Flash
EEPROM w/ ECC
5
ISO
IEC
  Note :Above reflects max configuration of each module – some functions are multiplexed.
Fail Safe Detection
Memory Protection
Notes: Moving on to the TMS570LS31x series, so these are the new TMS570 devices that are being announced in September. These also based on the Cortex-R4 floating point, 180 MHz, up to 3 megabytes of flash, and then also with a EEPROM emulation in the flash up to 64K of that. Same safety features as the RM device. From a communications point of view and these too have the 10/100 Ethernet and these also have the FlexRay communication interface, also with a dedicated DMA. So like I was mentioning previously on the High End Timer having its own DMA, the FlexRay has its own DMA inside this device. It's called the FlexRay transfer unit and it's also designed to handle the high bandwidth of the FlexRay communication protocol and not tying up the main system DMA or the CPU with FlexRay messages. And for those of you that haven't heard of FlexRay before, it's been primarily used in automotive up until now. We do see a lot of interest in other industries, even outside transportation for FlexRay, but it's primarily in communication. Aerospace is looking at it very heavily. Some people are saying, “Hey, this could be the next CAN.” It provides 10 extra bandwidth of CAN and it's very deterministic, so everybody on the FlexRay network essentially has a time slice where they have to communicate, so very good for safety applications, very good for applications that need a very deterministic communications network.
Now, moving on to the other peripherals in the 570LS3X: There are three CAN interfaces. There's also a total of five SPIs, so three multi-buffer, two standard. There's also two UARTs, and one of them also supports the automotive LIN 2.1 communications protocol. And then there's also an I2C. These devices also have the two High End Timers, 2 12 bit A to Ds and then also the 16 general purpose I/O pins that are also capable of generating interrupts. These devices also are in the same 144-pin QFP and 337 BGA. And these devices since they often do go into automotive applications have -40 to 125 C temperature operation.

## Slide 6
TMDXRM48HDK – RM48 Development Kit
TMDX570LS31HDK – TMS570 Development Kit
TMDX470MF066HDK – TMS470M Development Kit
    板载 USB XDS100v2 JTAG 调试器
    JTAG调试接口以便外接高性能仿真器
    TRACE连接点以便使用 ETM/RTP/DMM功能
    LED, 温度传感器和光传感器
    CAN收发器
    RJ45 10/100以太网
    USB-A 主机接口
    USB-B 设备接口
HerculesTM 开发环境
开发套件提供的软件包括:
    CCStudio v4.x IDE: C/C++ 编译器/链接器/调试期
    HALCoGen 外设驱动生成工具
    CCS 和 nowFlash 闪存编程工具
    HET GUI/仿真器
    GUI 演示程序及源代码示例
开发板
评估板
TMDXRM48USB – RM48 USB Stick Kit
TMDX570LS31USB – TMS570 USB Stick Kit
TMDX470MF066USB – TMS470M USB Stick Kit
    USB供电
    板载USB XDS100v2 JTAG 调试器
    板载SCI用于连接PC
    提供信号测试点可选择信号进行测试
    LED, 温度传感器和光传感器
    加速度计
    CAN 收发器
$79
$199
6
Notes: So moving on, to get customers started and going with development, we've created low cost tools. And like I said these are going to be available for order once we announce on September 6. And we’ve kept the same concept across our Hercules family, so our development kits are all priced the same whether you're getting started with a TMS470M or 570 or an RM4, and you have two main options. You have an evaluation USB stick. These are priced at $79. These are totally USB powered. They have an on-board JTAG emulator. They also have a UART to PC or SCI to PC serial communications channel. We provide access to select signal test pins on these boards. They also have an array of LEDs, temperature sensor and light sensors. There's also an accelerometer on the newer devices for the RM4 and the 570. And then there's also a single CAN transceiver on here and we're had these kits out for the 470 and the older 570s for over a year now. I’m amazed every time I go into a customer that’s had one of these for a few months and seeing the stuff that they're doing with it. I've always been amazed they developed little boards that plug on here. They developed boards that these plug into. They interface with their CAN network. It's pretty amazing what the customers can do with this very inexpensive hardware.
Then we also have full featured development kits shown here in the middle. These are all going to be priced at $199 available for again the 470M, the 570 and the RM. These also feature an on-board JTAG emulator. There's also a port on here. There are actually two connectors on here that provide customers the ability to use their higher end JTAG emulators. For doing real serious development, having a high speed JTAG emulator is very important for customers. A lot of them already have them from previous projects, so we have connectors on this board where they can plug those in. We also have trace pads for some of the trace modules, the ETM, RTP and DMM, again, the same array of LEDs with the temperature sensor and the light sensor mainly for demo purposes. These boards do feature two CAN transceivers and then on the RM4 specifically and the 570LS3, we have the 10/100 Ethernet interface, and then on the RM specifically we've got the USB-A host interface and USB-B device interface.
And then from a software point of view, the software that’s included in all these kits, so they come with Code Composer Studio version 4.0 Integrated Development Environment and these are not code size limited, not time limited, but they are tied to the development board. Then we also have HALCoGen. I'll go into more details on that in the next slide. Then we also have flash programming support integrated into Code Composer Studio and with a standalone nowFlash tool. Then we have the High End Timer graphical user interface and then we also have our demo software with a project and source code examples.

## Slide 7
RTOS
IDEs (编译器和调试器)
HerculesTM 软件开发工具
HALCoGen
用户可输入高抽象性的信息
图形界面的代码生成器
简易配置
新项目快速上手
支持 CCS, IAR & KEIL IDEs
PLL 计算器
帮助用户非常简单的配置Hercules平台的PLL和FPLL。
HET IDE
图形编程环境
输出模拟工具
生成可用于CCS环境的软件模块
包含了TI提供的一些功能例程
安全型MCU演示程序
演示了安全关键的性能
光线传感器和温度传感器演示
LED 演示
迷宫游戏演示
通过CCS浏览源代码
now Flash Flash编程工具
GUI和命令行的编程工具，无需IDE即可实现对Hercules产品的编程
GUI方式的代码生成工具和其他软件工具
now ECC ECC 生成工具
命令行工具以生成Hercules产品的ECC
可以配合CCSv4使用
提供编程/调试功能的IDE开发环境:
Code Composer Studio
IAR Workbench
KEIL µVision
实时操作系统：
SAFERTOS: High Integrity Systems
µC/OS: Micrium
ThreadX: Express Logic:(planned)
Notes: So going into software details a little bit more, so like I've mentioned previously, IDEs that we're promoting, so obviously Code Composer Studio but also IAR and KEIL have good support for the Hercules family. From an operating system point of view, the three main ones are SAFERTOS from High Integrity Systems, Micrium’s microC/OS and then also from ThreadX – or expresslogic, the ThreadX operating system. This one’s planned to be out a little further this fall, so not immediately available in September but soon after that. And the reason for promoting these is because all of these providers have safety-critical versions of their operating system, which is very important to our customers. If they're going to run an operating system, it has to be safety certified either that or the end customer has the burden of certifying the operating system. So we see several customers already using these three operating systems for their safety-critical applications.
Then a little bit more on the software, so the safety demos. So these highlight some of the safety features inside the device. Also, they use that ambient light sensor and temperature sensors to do a demo that are on the development boards. LED lights show, we have a maze game, and then the source codes viewable inside Code Composer Studio. We also have some graphical user interface tools to help configure the PLLs, the High End Timer Integrated Development Environment, and then HALCoGen. This is huge. If you’ve heard of the Grace tool for MSP430, this is very similar to that tool. And actually HALCoGen has been in development for over eight years now, and it provides a graphical user interface to go configure the chip. It generates start up code and it also generates peripheral drivers so people don’t have to spend a lot of time looking at the data book before they can start using the microcontroller. And we actually use this in our one-day class to actually do two hands on labs where we generate code for the microcontroller and we actually develop a UART, a UART driver, and we actually use that in our one-day class to get people going on the USB stick. It's a very powerful tool. And it also supports Code Composer Studio, IAR and the KEIL IDEs, so it generates code that’s compliable by all those compilers. We also have a command line tool for generating the ECC bits for the flash. This can be used in conjunction with the IDEs and as a post compile operation. And then we have a standalone tool available both in GUI and command line format for doing standalone flash programming of the microcontrollers.

## Slide 8: 寻求更多信息？
RM4 官网地址： www.ti.com/RM4
TMS570 官网地址： www.ti.com/TMS570
TMS470M 官网地址： www.ti.com/TMS470M
  数据手册 / 技术参考手册 / 应用手册
  软件和工具下载及更新
  订购评估板和开发工具
RM4，TMS570 和 TMS470M 的E2E论坛： http://e2e.ti.com/support/microcontrollers/hercules/default.aspxx
  新闻与公告
  有用的链接
  提交技术问题
  寻找技术文档
RM4 WIKI：
http://processors.wiki.ti.com/index.php/Category:RM4
TMS570 WIKI:
http://processors.wiki.ti.com/index.php/Category:TMS570
TMS470M WIKI:
http://processors.wiki.ti.com/index.php/Category:TMS470M
  如何入手
  介绍视频
  常用信息
RM Web Support
Coming Soon
TI Confidential – NDA Restrictions
Notes: So where can you to go get more information? So, I have the 570 and 470M publicly available webpages listed here. You can go out here. There's also going to be an RM page available starting September 6. It's not available right now but on these main webpages off at ti.com, you can get data sheets, technical reference manuals, application notes, all of the software that I mentioned is available for download. You can also get updates of the software here and then you can also order the evaluation and development kit, so the USB stick and the what we're calling the Hercules development kits, the full featured kits are available for order off of these pages. Then we also have a fully supported engineer-to-engineer forum. The ones that are up today are for the 570 and the 470M. And we have people on our applications, systems and design teams monitoring this forum and definitely our goal is to provide answers within 24 hours to any question that comes through here, and we’ve had very good feedback on support using these. If there are customers that have proprietary information that aren't comfortable posting on these forums, we do have an internal forum as well that’s set up where TI people in the field can ask those questions and then also it's searchable by people just internally in TI as well to get information. Then we also have Wiki set up for the 570 and 470. We will have one for the RM4, as well. Out here, we've got how to guides. We got introduction videos. We've got general information. We've also got code examples out there. We've got several step-by-step guides on how to generate code using HALCoGen for the device. We've also got introductory videos on how to use HALCoGen in our development kits. We also have introduction to safety video out there, as well. So these are some of the resources that are available to get more information on the Hercules microcontrollers.

## Slide 9: 1天的培训课程: Hercules 1天安全研讨会 3 天的培训课程: 如何使用ARM® CortexTM-R4F内核的Hercules系列产品进行安全关键类应用的设计和编程
Day 1
Day 2
Day 3
欢迎和介绍
Hercules产品介绍和Roadmap
安全标准和Hercules系统产品的安全特性
HALCoGen的使用 / 练习
Code Composer Studio开发环境的演示 / 练习
编译器 / 练习
Flash概览
Flash工具: nowFlashTM, nowECCTM, nowProfileTM
总结 / 提问
ARM ® Cortex™ -R4F 内核架构
系统模块概览
芯片的启动，实时中断，嵌套中断管理
CRC控制，CPU比较模块，错误信号模块
通用I/Os
直接存储器存取 (DMA)
串行通信接口(SCI/UART/LIN)
总结 / 提问
多级缓冲串行通信外设 (SPI / MIBSPI-P)
DCAN
FlexRay / 收发器
多级缓冲ADC(MIBADC)
外接存储器接口 (EMIF) / 参数覆盖模块 (POM)
高端定时器模块NHET 的 IDE
NHET
NHET Transfer Unit
总结 / 提问
面向的用户:
硬件和软件开发人员
项目管理人员
安全类应用专业人员
任何对Hercules MCU和安全模块感兴趣的人员
HerculesTM 培训课程
介绍
什么是安全功能？
安全标准
IEC 61508 安全标准
ISO 26262 安全标准
随机的故障管理
安全系统架构
Hercules 安全部件
Lab 1: Hercules 安全应用演示
Hercules 架构
开发工具: 开发套件，软件工具
内置Flash编程工具
实时中断 (RTI)
嵌套式中断管理 (VIM)
直接存储器存取 (DMA)
通用I/O口(GIO) & NHET
Lab 2: 将NHET用作GIO
通信外设: UART, LIN, CAN, FlexRay, Multi-Buffered Serial Peripheral Interface (MibSPI)
Lab 3: 通过SCI与PC通信
外接存储器接口(EMIF) / 参数覆盖
多级缓冲ADC (MibADC)
各类资源：网站，论坛，WIKI
Notes: Also very important is training. So we have two main classes that we offer and the first one is the one-day class and this one it – we're seeing that a lot of customers are new to safety. Either their end customer is requiring that their next generation device be qualified to one of the safety standards or a government body or some other entity is requiring that their next generation product be safety certified and they're somewhat – some of them are scared, some of them just don’t know what that means. So we have this one-day safety seminar set up that we basically spend the whole day or the whole first half of the day talking about the safety standards and what it means to be functionally safe. And then the last half of the day, we go into details about the Hercules microcontrollers and how they can be implemented in a safety-critical application and how customers can use the Hercules microcontrollers to easily implement safety in their system without having to learn about doing self-test algorithms themselves and how to test RAMs and that sort of thing.
And then like I've mentioned, these do have hands on labs as well—the first one where we run the safety demos then Labs 2 and 3 we actually use HALCoGen, Lab 2 here using the High End Timer as a GIO. We use HALCoGen to generate some code for us. We bring it into Code Composer Studio and then we blink one of the LEDs on the USB stick. And then Lab 3 here, we also use HALCoGen to generate a UART driver for us for the SCI module. And we do some bidirectional communication with the microcontroller. And usually these classes, when we offer them, we charge $79 admission and with that comes a USB stick development kit so that the engineers attending can take that home with them and continue with the TMS570 or Hercules application. And we've had great success giving these seminars and people that attend these seminars converting them over to design ins pretty quickly after attending. Then also we have a more in depth three-day class where we go into details into microcontrollers, so going into every communications module, every peripheral module in depth going into some of the tools in more depth and providing that detailed training for our customers.
So that’s the end of my presentation. I thank everybody for joining today.